# How Bridges Work BY ROBERT LAMB & MICHAEL MORRISSEY from How stuff works

We are a species of bridge builders. Since time out of mind, humans have engineered structures to surmount obstacles, such as, say, Jiaozhou Bay. The body of water is now home to a 26.4-mile (42.5-kilometer) bridge that links the busy Chinese port city of Quingdao to the Chinese suburb of Huangdou.

We've tamed steel, stone, lumber and even living vegetation, all in an effort to reach  places, people and things we desire.

## BATS: The Basics of Bridge Design

(Manitoba, Canada's Esplanade Riel pedestrian bridge)

If you're going to build a bridge, you'll need some help from BATS -- not the furry, winged mammals that so often live beneath bridges, but the key structural components of bridge  construction: beams, arches, trusses and suspensions.

Various combinations of these four technologies allow for numerous bridge designs, ranging from simple beam bridges, arch bridges, truss bridges and suspension bridges to more complex variations, such as the pictured side-spar cable-stayed bridge. For all its 21st century complexity, the side-spar design is based on suspension principles first used some two centuries earlier.

The key differences between these four bridge types comes down to the lengths they can cross in a single span, which is the distance between two bridge supports, the physical braces that connect the bridge to the surface below. Bridge supports may take the form of columns, towers or even the walls of a canyon.

Modern beam bridges, for instance, are likely to span up to 200 feet (60 meters), while modern arch bridges can safely cross 800-1,000 feet (240-300 meters). Suspension bridges are capable of extending from 2,000-7,000 feet (610-2,134 meters). Regardless of the structure, every bridge must stand strong under the two important forces we'll talk about next.

## Tension and Compression: Two Forces Every Bridge Knows Well

What allows an arch bridge to span greater distances than a beam bridge, or a suspension bridge to stretch over a distance seven times that of an arch bridge? The answer lies in how each bridge type deals with the important forces of compression and tension.

Tension: What happens to a rope during a game of tug-of-war? Correct, it undergoes tension from the two sweaty opposing teams pulling on it. This force also acts on bridge structures, resulting in tensional stress.

Compression: What happens when you push down on a spring and collapse it? That's right, you compress it, and by squishing it, you shorten its length. Compressional stress, therefore, is the opposite of tensional stress.

Compression and tension are present in all bridges, and as illustrated, they are both capable of damaging part of the bridge as varying load weights and other forces act on the structure. It's the job of the bridge design to handle these forces without buckling or snapping.

Buckling occurs when compression overcomes an object's ability to endure that force. Snapping is what happens when tension surpasses an object's ability to handle the lengthening force.

The best way to deal with these powerful forces is to either dissipate them or transfer them. With dissipation, the design allows the force to be spread out evenly over a greater area, so that no one spot bears the concentrated brunt of it. It's the difference in, say, eating one chocolate cupcake every day for a week and eating seven cupcakes in a single afternoon.

In transferring force, a design moves stress from an area of weakness to an area of strength. As we'll dig into on the upcoming pages, different bridges prefer to handle these stressors in different ways.

## The Beam Bridge

Bridge building doesn't get any simpler than this. In order to build a beam bridge (also known as a girder bridge), all you need is a rigid horizontal structure (a beam) and two supports, one at each end, to rest it on. These components directly support the downward weight of the bridge and any traffic traveling over it.

However, in supporting weight, the bream bridge endures both compressional and tensional stress. In order to understand these forces, let's use a simple model.

If you were to take a two-by-four and lay it across two empty milk crates, you'd have yourself a crude beam bridge. Now if you were to place a heavy weight in the middle of it, the two-by-four would bend. The top side would bend in under the force of compression, and the bottom side would bend out under the force of tension. Add enough weight and the two-by-four would eventually break. The top side would buckle and the bottom side would snap.

Many beam bridges use concrete or steel beams to handle the load. The size of the beam, and in particular the height of the beam, controls the distance that the beam can span. By increasing the height of the beam, the beam has more material to dissipate the tension. To create very tall beams, bridge designers add supporting latticework, or a truss, to the bridge's beam. This support truss adds rigidity to the existing beam, greatly increasing its ability to dissipate the compression and tension. Once the beam begins to compress, the force spreads through the truss.

Yet even with a truss, a beam bridge is only good for a limited distance. To reach across a greater length, you have to build a bigger truss until you eventually reach the point at which the truss can't support the bridge's own weight. Brace yourself for some serious stats on truss bridges on the next page.

## Truss Bridges: Beam Bridges With Braces

(Night lights illuminate the truss on Shanghai's Waibaidu Bridge.)

Travel around the world, and you'll encounter dozens of variations on your standard beam bridge. The key differences, however, all come down to the design, location and composition of the truss.

During the early Industrial Revolution, beam bridge construction in the United States was rapidly developing. Engineers gave many different truss designs a whirl in an attempt to perfect it. Their efforts weren't for naught. Wooden bridges were soon replaced by iron models or wood-and-iron combinations.

All these different truss patterns also factored into how beam bridges were being built. Some takes featured a through truss above the bridge, while others boasted a deck truss beneath the bridge.

A single beam spanning any distance undergoes compression and tension. The very top of the beam gets the most compression, and the very bottom of the beam experiences the most tension. The middle of the beam experiences very little compression or tension. This is why we have I-beams, which provide more material on the tops and bottoms of beams to better handle the forces of compression and tension.And there's another reason why a truss is more rigid than a single beam: A truss has the ability to dissipate a load through the truss work. The design of a truss, which is usually a variant of a triangle, creates both a very rigid structure and one that transfers the load from a single point to a considerably wider area.

While truss bridges are largely a product of the Industrial Revolution, our next example, the arch, dates back much further in time. Grab your sword and sandals, because we're about to go Roman.

## The Arch Bridge

(The Pont du Gard aqueduct is as old as the Christian religion.)

After more than 2,000 years of architectural use, the arch continues to feature prominently in bridge designs and with good reason: Its semicircular structure elegantly distributes compression through its entire form and diverts weight onto its two abutments, the components of the bridge that directly take on pressure.

Tensional force in arch bridges, on the other hand is virtually negligible. The natural curve of the arch and its ability to dissipate the force outward greatly reduces the effects of tension on the underside of the arch.

But as with beams and trusses, even the mighty arch can't outrun physics forever. The greater the degree of curvature (the larger the semicircle of the arch), the greater the effects of tension on the underside of the bridge. Build a big enough arch, and tension will eventually overtake the support structure's natural strength.

While there's a fair amount of cosmetic variety in arch bridge construction, the basic structure doesn't change. There are, for example, Roman, Baroque and Renaissance arches, all of which are architecturally different but structurally the same.

It is the arch itself that gives its namesake bridge its strength. In fact, an arch made of stone doesn't even need mortar. The ancient Romans built arch bridges and aqueducts that are still standing today. The tricky part, however is building the arch, as the two converging parts of the structure have no structural integrity until they meet in the middle. As such, additional scaffolding or support systems are typically needed.

Modern materials such as steel and prestressed concrete allow us to build far larger arches than the ancient Romans did. Modern arches typically span between 200 and 800 feet (61 and 244 meters), but West Virginia's New River Gorge Bridge measures an impressive 1,700 feet (518 meters)

## The Suspension Bridge

As the name implies, suspension bridges, like the Golden Gate Bridge or Brooklyn Bridge, suspend the roadway by cables, ropes or chains from two tall towers. These towers support the majority of the weight as compression pushes down on the suspension bridge's deck and then travels up the cables, ropes or chains to transfer compression to the towers. The towers then dissipate the compression directly into the earth.

The supporting cables, on the other hand, receive the bridge's tension forces. These cables run horizontally between the two far-flung anchorages. Bridge anchorages are essentially solid rock or massive concrete blocks in which the bridge is grounded. Tensional force passes to the anchorages and into the ground.

In addition to the cables, almost all suspension bridges feature a supporting truss system beneath the bridge deck called a deck truss. This helps to stiffen the deck and reduce the tendency of the roadway to sway and ripple.

Suspension bridges can easily cross distances between 2,000 and 7,000 feet (610 and 2,134 meters), enabling them to span distances beyond the scope of other bridge designs. Given the complexity of their design and the materials needed to build them, however, they're often the most costly bridge option as well.

But not every suspension bridge is an engineering marvel of modern steel. In fact, the earliest ones were made of twisted grass. When Spanish conquistadors made their way into Peru in 1532, they discovered an Incan empire connected by hundreds of suspension bridges, achieving spans of more than 150 feet (46 meters) across deep mountain gorges. Europe, on the other hand, wouldn't see its first suspension bridge until nearly 300 years later [source: Foer].

Of course, suspension bridges made from twisted grass don't last that long, requiring continual replacement to ensure safe travel across the gap. Today, only one such bridge remains, measuring 90 feet (27 meters) in the Andes.

## Cable-Stayed Bridge

Holland's Erasmus Bridge

At first glance, the cable-stayed bridge may look like just a variant of the suspension bridge, but don't let their similar towers and hanging roadways fool you. Cable-stayed bridges differ from their suspension predecessors in that they don't require anchorages, nor do they need two towers. Instead, the cables run from the roadway up to a single tower that alone bears the weight.

The tower of a cable-stayed bridge is responsible for absorbing and dealing with compressional forces. The cables attach to the roadway in various ways. For example, in a radial pattern, cables extend from several points on the road to a single point at the tower, like numerous fishing lines attached to a single pole. In a parallel pattern, the cables attach to both the roadway and the tower at several separate points.

Engineers constructed the first cable-stayed bridges in Europe              		         following the close of World War II, but the basic design dates back                    	      to the 16th century and Croatian inventor Faust Vrancic. A 	           contemporary of astronomers Tycho Brache and Johannes 	 	    Kepler, Vrancic produced the first known sketch of a cable-	    stayed bridge in his book "Machinae Novae."

Today, cable-stayed bridges are a popular choice as they offer all the advantages of a suspension bridge but at a lesser cost for spans of 500 to 2,800 feet (152 to 853 meters). They require less steel cable, are faster to build and incorporate more precast concrete sections.

## Additional Bridge Forces: Torsion and Shear

Torsion, for instance, is a particular concern for engineers designing suspension bridges. It occurs when high wind causes the suspended roadway to rotate and twist like a rolling wave. As we'll explore on the next page, Washington's Tacoma Narrows Bridge sustained damage from torsion, which was, in turn, caused by another powerful physical force

The natural shape of arch bridges and the truss structure on beam bridges protects them from this force. Suspension bridge engineers, on the other hand, have turned to deck-stiffening trusses that, as in the case of beam bridges, effectively eliminate the effects of torsion.

In suspension bridges of extreme length, however, the deck truss alone isn't enough protection. Engineers conduct wind tunnel tests on models to determine the bridge's resistance to torsional movements. Armed with this data, they employ aerodynamic truss structures and diagonal suspender cables to mitigate the effects of torsion.

Shear: Shear stress occurs when two fastened structures (or two parts of a single structure) are forced in opposite directions. If left unchecked, the shear force can literally rip bridge materials in half. A simple example of shear force would be to drive a long stake halfway into the ground and then apply lateral force against the side of the upper portion of the stake. With sufficient pressure, you'd be able to snap the stake in half. This is shear force in action.

# Text boxes

The Millau Viaduct spans the Tarn River Valley in Southern France.